## Slide 1: Recitation 2
Mini Lecture

## Slide 2: Office Hours
Hyungjoo Choi
Email: hc667@scarletmail.rutgers.edu Office Hours: Tuesday 3:30-4:30 PM Thursday 3:30-4:30 PM School of Engineering Building, room B114A

## Slide 3: Outline
Part 1: Recall Binary logic and math review
Part 2: User input and displaying output in scripts
Part 3: MATLAB Help

## Slide 4: Recall the rules of binary addition and subtraction
011
+ 100
3
+ 4
011
+ 100
111
3
+ 4
7
Same rules as base 10, just in base 2!
010
+ 011
2
+ 3
010
+ 011
1
2
+ 3
5
010
+ 011
01
1
Value carries
010
+ 011
101
110
- 001
6
- 1
110
- 001
1
6
- 1
5
110
- 001
01
-1
110
- 001
101
...But the negative value moves over to next digit
0 – 1 results in a 1...
-1
Notes: Walk students through these or similar examples. Make explicit note of the fact that numbers have to carry over to lead into the next slide.

## Slide 5: Recall operations
All math in computers needs to be accomplished via “logic gates”
  AND OR
  XOR NOT
Bit1 | Bit2 | Bit1 AND Bit2
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
Bit1 | Bit2 | Bit1 OR Bit2
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
Bit1 | Bit2 | Bit1 OR Bit2
0 | 0 | 0
1 | 0 | 1
0 | 1 | 1
1 | 1 | 0
Bit1 | NOT Bit2
0 | 1
1 | 0
Notes: These are the logical commands (along with their inverses) that can be built with transistors. While most logic gates now just use a large combination of NAND gates (NOT AND) due to the simplicity of components for building that, the overall concept on this slide is still true. While humans can think abstractly and do things like carry numbers, computers have to build abstraction from basic units (like with bits and representing data).

## Slide 6: Logic in MATLAB – Lecture 2
Logic
bit1 = 0; %MATLAB doesn't require you to declare something as a boolean
bit2 = 1; %As a result, any number that *isn't* 0 is "true"
%Just use 1's and 0's for logic, it can get confusing fast, otherwise
xorBit = xor(bit1,bit2); %Syntax for XOR
andBit = bit1 && bit2; %Syntax for AND
orBit = bit1 || bit2; %Syntax for OR
notBit = ~bit1; %Syntax for NOT

## Slide 7: Mathematical Operators – Reminder!
What are some mathematical operators in MATLAB?
Math
Name | Symbol/Function | Syntax Example
Addition | + | x = a+b;
Subtraction | - | y = a-b;
Negative | - | z = -x;
Multiplication | * | g = z*x;
Division | / | m = a/x;
Exponent | ^ | n = m^b;
Square Root | sqrt() | r = sqrt(a);
Natural Log | ln() | s = ln(b);
Absolute Value | abs() | t = abs(z);
If there is a mathematical operation you want to perform, it probably exists in MATLAB. Use the help button to find it.

## Slide 8: What are these built in functions?
There are only so many characters for operations to have in syntax
All other operations are in “function” form
bit3 =
bit3 = xor
bit3 = xor(bit1,bit2);
Built-In Functions
Output of function: The result of the calculation
Function name
Function inputs: Can put values or variables here.
bit3 = xor(1,0);
x = abs(-20);
Different functions have different numbers of inputs. Sometimes the order of inputs matters. Search for the function using the help button if you have issues.

## Slide 9: What are these built in functions?
There are only so many characters for operations to have in syntax
All other operations are in “function” form
x = abs(-20)*a + b;
Different functions have different numbers of inputs. Sometimes the order of inputs matters. Search for the function using the help button if you have issues.
You can use functions as part of a larger equation. In this case, the output of the function will be used in the overall calculation.
Built-In Functions

## Slide 10: Please follow along with me as I write a user input script that displays an output
Input function: input('How long is the rectangle?');
Output function: disp(area)
Can display a string before displaying a variable to give the display some context:
disp('The Rectangle has an area of')
disp(area)

## Slide 11: Wait, how does that thing in MATLAB work again?
The help window! It’s really useful!

## Slide 12: Naming a script – Reminder!!
Scripts must follow the same naming rules as variables when you save them
  No spaces  my script
  No special characters  #$*!@script
  Underscores OK  my_script
  Can’t start with numbers  1coolScript
Usually a good idea to name your script after what it does
  CalculateMyGrade
  findThePressure
Scripts and I/O

## Slide 13: Today you will simulate simple binary addition and subtraction in MATLAB